## Slide 1
参数请必须严格按以下规定来设定 Parameter set must comply with the following rules:
他他米面积在40MM*40MM以下的他他米长调4.5或视情况调到4，运行平针长最少要保持在2.5以上，最小针步：0.6，偏移系数也可以视情况调整，一般是0.25。The square measure of the Tatami is ≤40mm, then adjust the Tatami length to be 4.5mm or 4
And keep the regular stitch length above 2.5mm and the minimum stitch length 0.6mm and the offset is 0.25
他他米面积在40MM*40MM以上的他他米长全部调5，运行平针长3，最小针步：0.6，默认偏移：0.75
The square measure of the Tatami is ≥40mm, then adjust the Tatami length to be 5mm,
And keep the linear running stitch length above 3mm and the minimum stitch length 0.6mm, the offset is 0.75
一般的平针长度都要在2.5以上。贴布线和压线的长度要调到3。如果包边和贴布是同色的，不需要用疏挨针压贴布。行线两次即可。一般行线包边的平针长度为2,走两次。
Ordinary stitch length is above 2.5. Applique stitch length and applique placement stitch length should be 3. if the colors of the applique and the sewn down thread are the same, it is ok to use double running stitch applique placement instead of zigzag applique stitch placement.
It is ok to do double running stitch with stitch length 2mm for running sewn down pattern.
一定不能把“可变平针长度”选项打勾！！！
他他米一定要在车下缝前行沿他他米四周走一圈行线，面积大的走两次或走一圈3MM以上宽的疏挨针
Tatami should be with a running stitch around the border, if the Tatami is with large area,
double running stitch or 3mm zigzag stitch around the border of Tatami if it is necesarey
细挨针打底在中间走行线就行了，6MM以上的宽挨针打底要在中间和两边都走行线。所有挨针不用下缝
For the tiny satin stitch it is ok to have intermediate stitch,
If the width of the satin underlay stitch is above 6mm, it should have a running stitch in the middle and both borders ,
 | 浅色布车撞色线stitch on light color fabric | 浅色布车同色 线 the thread color is similar to the light fabric | 深色布车撞色线 Stitch on dark color fabric | 深色布车同色线 the thread color is similar to the dark fabric | 底布与线不同色的 Both of the color for the thread and the ground fabric are different.
他他米面线密度density of the face thread for Tatami stitch | 0.42 | 0.65 | 0.42 | 0.6 | 0.42
他他米下缝密度density of the Tatami inset | 2 | 不用下缝 no need inset | 1 | 不用下缝 no need inset | 1.5
偏移系数 Offset value | A:0.75 B:0.75 | A:0.25 B:0.25 | A:0.75 B:0.75 | A:0.25 B:0.25 | A:0.75 B:0.75
挨针密度 | 0.38 | 0.55 | 0.38 | 0.55 | 0.42
尺寸大的花一下要从中间往两边绣，包边多的多分几次包！尽量减少剪线，转色，短针步。
Stitch from the middle to the both borders for the emblem with big size ,
Emblem with individual part , it should be sew down by segments , try to make less thread cut, color change and short stitch.

## Slide 2
图形不对称design with dissymmetry
改对称后图形更美观 pattern looks better after edition with symmetry
客来图中间小字母与两边挨针
的距离不分中 the space in between the small letters on customer’ artwork is inconsistent.
改成分中后字母清晰可见，花样更美观
Letters looks more clean after edition

## Slide 3
字母的间距不均匀,高低不一致 The space and height between the letters are uneven.
做相应的调整使其均匀并一致 Do some proper adjustment to make the letters be consistent.

## Slide 4
有些客户来的图稿字母之间的间距不统一，可相应的调整字母的间距使其美观（图A），或适当的靠近，使其可以方便连线车。（图B）Space between letters on the artwork provided by a few of customer are inconsistent.
It is necessary to do proper adjustment and make the letters be even and it be convenient for connect stitching.
A
B

## Slide 5
如果小字母的高度小于3.5MM
if the height of the small letters ≤3.5mm
可在10-20%的规定范围内自行放大小字母。
The letters can be increased by 10-20%
如果已经没有空位可以放大，则可以改成行线车。If there is no space for increasing , the letters can be changed to running stitch.

## Slide 6
客户要求取消字母“CROCKER LEGACY” Customer requires to delete the letters “CROCKER LEGACY”
马头相应的往下移一点,
甚至可以稍微放大点。
The horse head can move down a little bit
Or enlarge the horse head a little.
那么整个花样看上去就会比较美观协调。The whole pattern can looks more perfect .
显得太空洞了 this area looks empty.

## Slide 7
应该适当的把狮子图案放大
The lion should be enlarged properly
客户要求取消上面图案
Customer requires to remove the pattern
Above the lion.
那么整个花样看上去就会比较美观协调。The whole design can looks more perfect.

## Slide 8
所有高度在4MM以下的小字母或小对象以及挨针宽度小于1.2MM的小花型
The tiny letters which height is less 4mm or the width of the satin stitch is under 1.2mm.
都必须拉长针（长度5mm以上，方便手工剪线）出去车，然后用手工剪线。
All the stitch must be lengthened ( the length is above 5mm, it will be convenient for thread cut by hand.
相对大点的对象和小字母则应该注意在下针的时候下两到三针短针步，以令其能拉起底线，并在锁针时留意锁针的方法。锁紧，不要让其掉线。
For the small letters, inset two or three short stitch and pay attention to the direction of the lock stitch and lock tightly to avoid thread missed as penetrating for pull up the bobbin thread,
4mm以下
小于1.2mm
由于机器下针的前两针一般是很难拉起底线的，且在下针和剪线的时候都会有一个小线团，严重影响花样的美观。
It will be difficult for the machine to pull up the bobbin thread at the first two stitches and there will be a small clew as penetration or thread cut, finally affect the embroidery looking.
有些客户会要求每个字母都要剪线 some of customer requires each letter should be trimmed

## Slide 9
字母高度
height of the letters >4mm
不用拉长针
No need to lengthen the stitching
字母高度<4mm
height of the letters >4mm
要拉长针
Stitching must be lengthened.
字母间距space in between letters <0.4mm 可连线 thread can be connected
字母间距space in between letters >0.4mm 剪线 thread should be cut.

## Slide 10
字母间距<0.4MM 可以连线 space in between letters <0.4MM, thread can be connected.
但要注意箭头所指画绿线处小字母与红色挨针以及兰色挨针的距离要一致。上下分中。
The distance between the small letters highlighted by green lines and red / blue satin stitch should be consistent.

## Slide 11
由于绣花机的极限刺绣宽度是12.7MM,因此一般超过8MM的针步就会很难车，现规定如下：
Due to the limited stitch width for the multihead machine is 12.7mm, it will be have some difficult for the stitch width over 8mm, thus the regulation is set as following :
所有宽度超过8MM的挨针，不论是客来原办或是客来Artwork，都将其改成叉针（图1）或分割（图2）
All 8mm satin stitch should be changed to cross stitching even if it is a copy from customer’ supplied sample or artwork.